## Slide 1
DDCA PROJECT · BATCH 2
MODULE 3
Design of a Four-Bit Binary
to Decimal Conversion
Module 3 Basics: Sequential Logic — Giving the Machine Memory
A quick look at how registers, counters and flip-flops — the memory elements our converter itself doesn't need — can still be used around it to hold its input and test it automatically.
DDCA PROJECT · BATCH 2 · MODULE 3
1 / 17

## Slide 2
OVERVIEW
What This Project Uses From Module 3
1
Registers
A row of flip-flops that could hold our 4-bit input steady before decoding.
2
Counters
A simple way to automatically cycle through all 16 inputs to test our decoder.
3
Clock & timing
The idea of a clock edge, so stored values change at a known, reliable moment.
4
FSMs (just the idea)
Our decoder itself doesn't need one — but we see where it would fit in a bigger system.
DDCA PROJECT · BATCH 2 · MODULE 3
2 / 17

## Slide 3
AN IMPORTANT DISTINCTION
Our Converter Is Combinational — Here's the Contrast
COMBINATIONAL (our converter)
Output depends only on the current input
No clock, no memory, no “state”
Built from gates: NOT, AND, OR …
SEQUENTIAL (this module)
Output depends on current input AND what was stored before
Needs a clock to know exactly when to update
Built from latches, flip-flops and registers
DDCA PROJECT · BATCH 2 · MODULE 3
3 / 17

## Slide 4
BASIC MEMORY ELEMENTS
Latches & Flip-Flops: The Basics
SR Latch
The simplest memory cell — Set makes it 1, Reset makes it 0, and it holds that value otherwise.
D Latch
Stores whatever is on its D input, but only while a control signal is “open” (level-sensitive).
D Flip-Flop
Stores the D input at the exact instant the clock ticks (edge-triggered) — the building block of registers.
Level-sensitive (latch) reacts whenever the control signal is high; edge-triggered (flip-flop) reacts only at the instant the clock changes — flip-flops are what real registers use.
DDCA PROJECT · BATCH 2 · MODULE 3
4 / 17

## Slide 5
KEEPING TIME
The Clock & Synchronous Design
A clock signal ticks at a steady rate, so every flip-flop in a circuit updates at the same, predictable moment.
This “synchronous” design is what makes large digital systems reliable — everything changes in step, rather than drifting out of sync.
Setup and hold time (just the intuition): each flip-flop's input needs to be stable for a brief moment just before and just after the clock edge, or its stored value can't be trusted.
DDCA PROJECT · BATCH 2 · MODULE 3
5 / 17

## Slide 6
STORAGE ELEMENTS
Registers: Holding Our 4-Bit Input
A register is just 4 D flip-flops side by side, one per bit — enough to store one 4-bit value at a time.
Our decoder itself has no memory, but in a real system its input would usually come from a register, so the value stays steady while the decoder reads it.
CLOCK
4-BIT
REGISTER
OUR
DECODER
Y0–Y15
clock tells the register exactly when to latch a new value
DDCA PROJECT · BATCH 2 · MODULE 3
6 / 17

## Slide 7
A CLOSE RELATIVE
Shift Registers (Brief)
A shift register is a chain of flip-flops where, on every clock tick, each bit moves into its neighbour — the whole value shifts left or right by one position.
It's useful for turning a stream of single bits into a parallel value (or back again) — for example, receiving a 4-bit number one bit at a time over a single wire, then reading all 4 bits at once.
Our project doesn't need one: the 4-bit input to our decoder already arrives as 4 bits side by side, so there's nothing to shift in or out.
DDCA PROJECT · BATCH 2 · MODULE 3
7 / 17

## Slide 8
A PERFECT USE CASE
Counters: Auto-Testing Our Decoder
A synchronous counter is a register that adds 1 to itself on every clock tick — the same pattern used for a CPU's program counter, which tracks “which instruction is next.”
For our project, a 4-bit counter is a natural testbench: let it count 0000 → 1111 automatically, feed each value into our decoder, and watch Y0 through Y15 light up in order.
CLOCK → 4-bit counter: 0000, 0001, 0010, …, 1111 → our decoder → Y0, Y1, Y2, …, Y15
DDCA PROJECT · BATCH 2 · MODULE 3
8 / 17

## Slide 9
SCOPE CHECK
Finite State Machines — Not Needed Here
An FSM describes step-by-step behaviour using states and transitions — it's the technique behind a control unit.
Our decoder has no steps to follow: it just reads 4 bits and lights one output, all in one go — there's no “next state” to transition to.
FSMs matter for this module because a real control unit — deciding what a CPU does next, instruction by instruction — is exactly this kind of step-by-step machine.
DDCA PROJECT · BATCH 2 · MODULE 3
9 / 17

## Slide 10
FROM SPEC TO STATES
Designing a Small FSM: A Test Controller
A worked example — an FSM that could drive the counter testbench from Slide 8.
IDLE
Waiting for a start signal. Counter is held at 0000.
RUN
Counter increments every clock tick, feeding our decoder.
DONE
Counter reached 1111; all 16 outputs have been tested.
Specification → states and transitions → flip-flops to hold the current state → logic to decide the next state. This is the exact same disciplined flow used for a real CPU control unit.
DDCA PROJECT · BATCH 2 · MODULE 3
10 / 17

## Slide 11
FROM DIAGRAM TO TABLE
The Test Controller as a State Table
The same IDLE → RUN → DONE machine, written the way an FSM is usually implemented
Current State | Input / Condition | Next State | Action
IDLE | start = 1 | RUN | RegWrite counter ← 0000
IDLE | start = 0 | IDLE | hold — no change
RUN | count < 1111 | RUN | counter ← counter + 1
RUN | count = 1111 | DONE | stop incrementing
DONE | — | DONE | hold — test finished
A state table is just the state diagram's arrows written as rows — both describe the exact same machine; the table is what you'd hand to a flip-flop-and-gate implementation.
DDCA PROJECT · BATCH 2 · MODULE 3
11 / 17

## Slide 12
MODULE DELIVERABLE
Milestone: Register, Counter & a Small FSM
Register
A 4-bit register built and tested in the simulator, holding one steady value.
Counter
A synchronous counter cycling 0000 through 1111 on its own, clock tick by clock tick.
Small FSM
The IDLE → RUN → DONE controller from the previous slides, built from flip-flops and logic.
Together, these three pieces are the CPU's “memory-and-stepping fabric” — and, for this project, a complete automatic test rig for our decoder.
DDCA PROJECT · BATCH 2 · MODULE 3
12 / 17

## Slide 13
COMBINING BOTH WORLDS
Putting It Together
Sequential part
Clock + counter (or register) — remembers a value and steps it forward in time.
Combinational part
Our decoder — instantly turns whatever 4 bits it's given into one lit output.
Most real systems are exactly this mix: sequential elements that remember and step through time, driving combinational logic that reacts instantly — which is also how a full CPU works.
DDCA PROJECT · BATCH 2 · MODULE 3
13 / 17

## Slide 14
A PRACTICAL DETAIL
Resetting a Register: Sync vs Async
Every register or counter needs a known starting value — this is how it gets one.
SYNCHRONOUS RESET
The reset signal is only obeyed on the next clock edge — it waits its turn like any other input, which keeps every flip-flop changing in step.
Our counter would use this: on the IDLE → RUN transition, it's told “counter ← 0000” as an ordinary clocked update.
ASYNCHRONOUS RESET
The reset signal clears the flip-flop immediately, regardless of the clock — useful for forcing a known state the instant power turns on.
Faster to react, but it can ignore the clock entirely — which is why most classroom designs prefer the synchronous version.
DDCA PROJECT · BATCH 2 · MODULE 3
14 / 17

## Slide 15
STUDY AID
Module 3 Quick Reference
Latch
Memory cell that reacts whenever its control signal is high.
Flip-flop
Memory cell that reacts only at a clock edge.
Register
Several flip-flops storing one multi-bit value.
Clock
The steady signal that tells every flip-flop exactly when to update.
Counter
A register that adds 1 to itself every clock tick.
FSM
States + transitions describing step-by-step behaviour.
DDCA PROJECT · BATCH 2 · MODULE 3
15 / 17

## Slide 16
SUMMARY
Module 3 Takeaways
Our converter is purely combinational — it has no memory, which is exactly what sets it apart from everything in this module.
Latches and flip-flops are the basic memory cells; registers are just several flip-flops storing one multi-bit value, like our 4-bit input.
A counter is a register that increments itself every clock tick — a natural way to automatically test all 16 inputs of our decoder.
FSMs aren't needed for our one-step decoder, but they're exactly the tool — and a state table is exactly the format — for a real control unit later in the course.
DDCA PROJECT · BATCH 2 · MODULE 3
16 / 17

## Slide 17
Thank You
Design of a Four-Bit Binary to Decimal Conversion — Module 3 Basics
DDCA PROJECT · BATCH 2 · MODULE 3
17 / 17